# Application of Support Vector Machine to Ship Steering

LU Weili1* (卢伟李), ZHAO Dexiong（赵德熊）1, 2

(1. School of Naval Architecture, Ocean and Civil Engineering, Shanghai Jiaotong University, Shanghai 200240, China; 2. College of Civil and Architectural Engineering, )

Abstract: System identification is an effective way for modeling ship manoeuvring motion and ship manoeuvrability prediction. Support vector machine is proposed to identify the manoeuvring indices in four different response models of ship steering motion, including the first order linear, the first order nonlinear, the second order linear and the second order nonlinear models. Predictions of manoeuvres including trained samples by using the identified parameters are compared with the results of free-running model tests. It is discussed that the different four categories are consistent with each other both analytically and numerically. The generalization of the identified model is verified by predicting different untrained manoeuvres. The simulations and comparisons demonstrate the validity of the proposed method.

Key words: ship steering, parameter identification, response model, support vector machine

CLC number: U 661         Document code: A

## Nomenclature

A — Area, m2

## 0  Introduction

(The formal standard of ship manoeuvrability promulgated by the International Maritime Organization (IMO)[1] promotes the research on ship manoeuvrability. Mathematical model combined with computer simulation is an important method for ship manoeuvrability prediction at the stage of ship design[2]. System identification (SI) provides an effective way for modeling ship manoeuvring motion and subsequently the prediction of ship manoeuvrability, especially the SI with the advent of modern measurement equipments and advanced system identification techniques. Traditional system identification techniques for ship manoeuvring, such as the least squares (LS) method[3], the Extended Kalman Filter (EKF)[4-5], the Maximum Likelihood (ML) [6]and the Recursive Prediction Error (RPE)[7] etc., have some shortcomings in practical application, mainly including initial values of variables, ill-condition solutions, and simultaneous drift of parameters. Recently, a frequency domain analysis method was proposed to the identification of hydrodynamic coefficients[8-9]. However, this batch identification is restricted in the low frequency domain and the systems with weak nonlinearity. It is considered that several conditions are necessary for the high-precise identification of system parameters. The first one is the batch identification rather than the step iterative identification, since the batch one can prevent the dynamics cancellation effect. The second condition is the ability of avoiding the problem of dimension curse, which usually results in a very large condition number of the Gram matrix and subsequently ill-condition solutions. Finally, the time domain analysis is better than the frequency one while dealing with the nonlinear system. Fortunately, an advanced artificial intelligent technique, Support Vector Machine (SVM), was found to be satisfied the three above mentioned requirements. SVM learning strategy, based on the statistical learning theory, is a type of optimized model in which prediction error and model complexity can be simultaneously minimized[10]. It has found wide applications to system engineering during last decade and is considered to be a useful method in the field of system identification. It has two outstanding advantages. Firstly, this time domain batch algorithm is based on the criteria of structural risk minimization (SRM) and has good generalization ability. Secondly, the convex quadratic programming of SVM guarantees a global optimal solution. More details and mathematical descriptions about this machine learning method can be found in references[11-12].

This paper makes an effort to the parameter identification of the ship response model by using SVM. Four categories of the response model are considered. Predictions of manoeuvres including trained samples by using the identified parameters are compared with the results of free-running model tests. It is discussed that the four categories are consistent with each other. The generalization of the identified model is verified by predicting different untrained manoeuvres.

1  Response Model of Ship Steering Motion

The response model of ship steering motion, usually named Nomoto model or K-T model, includes simple parameters such as K and T indices which can be expressed by the hydrodynamic derivatives[13-14]. It reflects the relationship between the system inputs and outputs of a dynamic ship steering system, which has been found wide applications in ship manoeuvring and control. In this paper, four categories of response model are considered.

The first order linear model is

(1)

the first order nonlinear model is

(2)

the second order linear model is

(3)

the second order nonlinear model is

(4)

where ,and are manoeuvring indices;  is the yaw rate and  is the rudder angle;  is the initial deviation of rudder angle;  is the coefficient of linear term;  is the coefficient of nonlinear term; and .

2  Identification of Manoeuvring Indices

2.1 Parameter Identification

A series of free-running model tests were conducted in the seakeeping basin of the State Key Laboratory of Ocean Engineering in SJTU to supply the input-output data for the identification. The length of the model is , the draft is the service speed is , and the model scale is 1:50. Seven hundreds training samples are arbitrarily drawn from the data of the  zigzag manoeuvre rather than that of turning circles in consideration of efficient excitation.

After discretization, Eqs.(1)—(4) are deduced to the following expressions.

The first order linear model is

(7)

the first order nonlinear model is

(8)

the second order linear model is

(9)

the second order nonlinear model is

(10)

where k denotes the sampling time; and  are coefficients of model; the K, T indices in the continuous equation can be calculated after  have been identified. SVM is then applied to the parameter identification. Linear kernel function is adopted and the regularization factor is taken . The identification results are given as follows.

The parameters in the first order linear model are

In the first order nonlinear model, they are

In the second order linear model, they are

And in the second order nonlinear model, they are

Note that in the second order nonlinear model, the coefficient is set as one because of parameter identifiability, which is usually inevitable in the system identification of ship manoeuvring[4]. Nevertheless, from the viewpoint of system simulation or prediction, rather than from that of physical meanings, a few coefficients can be assumed as known beforehand.

2.2 Predictions of Ship Manoeuvring Motion

Substituting the parameters into the equations of ship manoeuvring motion, i.e. Eqs.(1)—(4), yields the overall histories of the yaw rates and headings. The predictions of ship manoeuvring motion in different cases are shown in Fig.1.

(a) The first order linear model             (b) The first order nonlinear model

(c) The second order linear model        (d) The second order nonlinear model

SVM prediction,         Test data

Fig. 1  Predictions of zigzag manoeuvre

The predicted overshoot angles and the overshoot angles in test are shown in Table 1.

Table1 Predicted overshoot angles and overshoot angles in test

| Model(test) | /K |  |
| --- | --- | --- |
| Test | 15.21 | 22.27 |
| Linear model (1st) | 11.45 | 16.04 |
| Linear model (2nd) | 11.37 | 15.79 |
| Nonlinear model (1st) | 13.84 | 16.40 |
| Nonlinear model (2nd) | 13.55 | 16.30 |

where is the first overshoot angle, is the second overshoot angle.

As seen from the comparisons between predictions and actual test results, the identified model characterizes the dynamics of ship. Moreover, the nonlinear model approximates better, especially for prediction of the first overshoot angle.

3  Model Comparisons and Generalization Verification

3.1 Model Comparisons

The four structures of the response models should be coincided mathematically because they reflect the same dynamics of the ship investigated. It can be confirmed by cross verification.

Firstly, the comparison is conducted between the first order linear model and the nonlinear one, as shown in Table 2.

Table2 Parameter relationship between the first order linear and nonlinear models

| Model structure |  |  |
| --- | --- | --- |
| Linear model (1st) | -0.090 | -0.053 |
| Nonlinear model (1st) | -0.092 | -0.062 |

Secondly, the comparison is between the first order linear model and second order linear model. The transfer function of the first order linear model can be obtained by Laplace transformation:

(11)

For the second order linear model, it is:

(12)

If the high frequency characteristics of the ship dynamics can be ignored, i.e. and [13-14], the above expression can be deduced to:

(13)

Obviously, the relationship of indices between two models aforementioned holds:

(14)

The numerical comparisons are given in Table 3.

Table3 Parameter relationship between the first order linear and the second order linear models

| Model structure |  |  |  |
| --- | --- | --- | --- |
| Linear model (1st) | -0.43 | 4.76 | -0.053 |
| Linear model (2nd) | -0.44 | 4.97 | -0.054 |

Finally, the second order linear model and the second order nonlinear model are compared by analogy, as shown in Table 4.

Table4 Parameter relationship between the second order linear and nonlinear models

| Model structure |  |  |  |  |
| --- | --- | --- | --- | --- |
| Linear model (2nd) | 20.61 | -1.83 | -0.20 | -0.054 |
| Nonlinear model (2nd) | 20.92 | -1.87 | -0.28 | -0.062 |

From the comparison results, it is concluded that the four structures are mathematically consistent.

3.2 Generalization Verification

For an artificial intelligent algorithm, the generalization verification is necessary[15]. It requires that the intelligent structure and parameters can well blindly predict the untrained samples. Because the different structures of response models are consistent inherently and the nonlinear model better characterizes the object in consideration. The first order nonlinear model is selected for the generalization verification. The verification samples are drawn from two different manoeuvres, including zigzag manoeuvre and starboard turning. Figure 2 shows the results of prediction.

SVM prediction,         Test data

Fig. 2  Prediction of zigzag manoeuvre

From the prediction results, it is concluded that the results of identified parameters are satisfactory. Notice that the approximation discrepancy of the second overshoot and thereafter in zigzag manoeuvre results from the experimental errors rather than the SVM method itself.

4  Conclusion

Prediction of ship manoeuvrability at the stage of ship design provides an important tool to evaluate ship manoeuvrability. Computer simulation based on mathematical model of ship manoeuvring motion is an effective and practical way to predict the ship manoeuvrability. Accurately determining the hydrodynamic coefficients in the mathematical model is vital to the prediction accuracy. In this paper, system identification based on SVM effectively determines the manoeuvring indices in the response models of ship steering motion, with respect to four different structures. The simulation results of the predictions of manoeuvring motion and the check of generalization demonstrate the verification and validity of the proposed intelligent method. It may be extended to the hydrodynamic model such as MMG model or Abkowitz model, if one has more abundant input-output samples. More efforts will be devoted to the verification and validity of benchmark ships provided by the International Towing Tank Committee (ITTC) or full-scaled ships.

Acknowledgement    The authors thanks to ……..

References

- Resolution MSC.137(76), Standards for ship manoeuvrability[S]. 2002.

- International Towing Tank Committee (ITTC). Report of maneuvering committee[C]// Proceedings of 24th ITTC. Edinburgh, UK: International Towing Tank Committee, 2005, 1:138-146.

- Sung Y J, Lee T I, Yum D J, et al. An analysis of the PMM tests using a system identification method[C]// Proceedings of the 7th International Marine Design Conference. Kyonyju, Korea: Local Organizing Committee, 2000:1-10.

- HWang W Y. Application of system identification to ship maneuvering[D]. Massachusetts, USA: Massachusetts Institute of Technology, 1980.

- Yoon H K, Rhee K P. Identification of hydrodynamic coefficients in ship maneuvering equations of motion by Estimation-Before-Modeling technique[J]. Ocean Engineering, 2003, 45(30):2379-2404.

- Åström K J, Källström C G. Identification of ship steering dynamics[J]. Automatica, 1976, 12(1): 9-22.

- Källström C G, Åström K J. Experiences of system identification applied to ship steering[J]. Automatica, 1981, 17(1):187-198.

- Selvam R P, Bhattacharyya S K, Haddara M R. A frequency domain system identification method for linear ship manoeuvring[J]. International Shipbuilding Progress, 2005, 52(1):5-27.

- Bhattacharyya S K, Haddara M R. Parameter identification for nonlinear ship manoeuvring[J]. Journal of Ship Research, 2006, 50(3): 197-207.

- Vapnik V N. An overview of statistical learning theory[J]. IEEE Transaction on Neural Networks, 1999, 10(5): 988-999.

- Vapnik V N. Universal learning technology: support vector machines[J]. NEC Journal of Advanced Technology, 2005, 2(2): 137-144.

- Vapnik V N. Statistical learning theory[M]. New York, USA:John Wiley & Sons, 1998.

- Nomoto K, Taguchi K, Honda K, et al. On the steering qualities of ships－Ⅰ[J]. Journal of Society of Naval Architects of Japan, 1956, 99: 75-82 (in Japanese).

- Nomoto K, Taguchi K. On the steering qualities of ships－II[J]. Journal of Society of Naval Architects of Japan, 1957, 101: 57-66 (in Japanese).

- Haddara M R, Wang Y. Parametric identification of maneuvering models for ships[J]. International Shipbuilding Progress, 1999, 46(445): 5-27.

- LI S, WANG G, WANG S, et al. Application of fracture-damage model to anchorage of discontinuous jointed rockmass of excavation and supporting [J]. Chinese Journal of Rock Mechanics and Engineering, 2006, 25(8): 1582-1589 (in Chinese).

# Footnotes

Received date: 2007-02-07

Foundation item: the Special Research Fund for the Doctoral Program of Higher Education (No. 20050248037) and the National Natural Science Foundation of China (No. 50779033)

* E-mail: wlo@sjtu.edu.cn

# Comments

通讯作者的标记Corresponding author’s mark

如果作者是同一单位的下属不同学院，则编号用a,b…并把同一单位写到最后，学院之间用分号隔开

逗号，不是分号Comma, not semicolon

中图分类号，没有写的请补充，不知道中途分类号是什么的，请google CLC number

如果文章中有很多符号说明，在这里统一给出符号说明，符号少于五个，只在正文中说明即可，这个部分删之

If there are many signature in paper, give nomenclature here

从0开始，而不是1

Begin from 0, not 1

上标

Superscript

第一次出现的缩写，要给出全称

Abbreviations used for the first time need to be written as the full name

连续引用参考文献的格式

Format of citing the successive references

每个实词的首字母大写

Capital initial letter of every notional word

公式后面有标点符号Punctuation after equation

Using Mathtype is encouraged

解释公式中变量的标准格式

Note use of comma and semicolon

数值和单位之间有半个格的空间

Space between number and unit

表示范围的符号，两个空格的长度，不会输入的请把这个符号拷贝过去

Use two spaces as a symbol for range, you can copy it in your manuscript

解释公式中的符号，开头请加where，注意开头w小写

“where”:  in lower-case letters instead of capitals

引用多个公式时的格式Use Eqs. when citing more than one equation

引用图形的格式Format of citing figure.

引用表格的格式，注意，不要缩写成Tab.

Format of citing Table

表格用三线表

Use three-line tables in sci_tech periodicals

表中单位的格式，如果unit

公式后没有参数说明，则用句点结束

Use dot in the end, if there is no interpretation about Eqs.

句子开头引用图时，不缩写Fig.

“Figure” is used at the beginning of the sentence and “fig.” is used in the middle or at the end of the sentences

不加s

No “s”

致谢的格式，注意这里只对人或机构进行感谢，基金项目写在首页页脚处

Use only when you should thank somebody or some institutions, not foundation item

参考文献为标准，用此格式

format of standard

会议文献的格式mark of conference reference

会议文献要列出出版者和出版地

Publishers and publish places should be listed

参考文献中的作者的格式，姓全部大写，名用缩写

format of author of reference

学位论文的格式mark of thesis

Publisher and publish place should be listed

图书专著\会议文献\规范标准等文献要求列出出版者和出版地

mark of journal reference

卷号用黑体，期号用括号

Volume number(issue number)

Volume number: boldface type

不管此文章发表时题名中单词首字母是否大写，这里引用时，题目中只有第一个词的首字母大写

Only the first letter of the first word in the title should written in capticals

Volume: Bold italic

卷号用黑斜体

Journal name: italic, and use full name

期刊名用斜体，并且用全称，不要用缩写

只列出前三个作者，其后作者用et al.

List the first three authors

表示这篇参考文献是日文的

means this reference is in Japanese

这篇参考文献是中文的

Means this reference is in Chinese